## Slide 1: Decision Workshop December 2016 Results of City Diagnostics & Draft Energy Efficiency Plan for Gjirokastra Municipality
ALBANIA: Project for Integrated Urban and Tourism Development (PIUTD)

## Slide 2: Agenda
Introduction
Municipal energy diagnostics and Sector prioritization
Energy efficiency challenges and opportunities by sector
Municipal energy efficiency plan - Investment program
Implementation strategy
decisions and next steps

## Slide 3: Urban Energy and Development Challenges
Economic and demographic challenges
Increasing:
Population growth
Demand for energy
Demand for municipal services
Maintenance and operations cost
Environmental emissions
Tourism activity in Gjirokastra
Overall municipal level energy challenges
Unreliable electricity and water supply challenges and along with increasing urbanization
Limited energy supply and services for public buildings
Limited capacities for preparation and implementation of energy saving and retrofit measures
Limited availability for investment finance
Limited capacities for enforcement of energy performance regulation
Generally low awareness of energy efficiency opportunities and behavior due to lack of information and low energy tariffs

## Slide 4: Objectives and Methodology
City Energy Efficiency Transformation
Energy Efficiency Improvement perspective for 10 -15 years
Solutions to achieve set targets: Reduction of energy consumption
Meet the requirement of the energy law: Set-up municipal energy management
Reduction of energy costs
Increase of comfort meeting actual needs
Delivery mechanisms
Decision Workshop
Overview of key challenges and opportunities
Discussion and setting of priorities and targets
Discussion of appropriate EE measures
Decision of appropriate EE measures for transformation program
Outlook on the municipal EE plan
Discussion of delivery mechanism and institutional set-up
City Background Report
Key Performance Indicators
Sector Priorities
EE Recom-mendations
DECISION WORKSHOP
Energy Efficiency Plan

## Slide 5: Turning Challenges into Opportunities
The current Energy Efficiency Law number 124 dated 12.11.2015; requests Albanian municipalities to
  prepare municipal energy efficiency plans (article 7)
  establish a municipal energy management department (article 25)
Create a momentum to commit to achieving EU energy and climate related targets at local levels
  participation in the EU Covenant of Mayors initiative (CoM)  elaboration of a Sustainable Energy Action Plan (SEAP).
  opportunities to exchange experience, gain related know-how, build capacities  acquire financial support from EU pre-accession programs
Development of EE investment projects and raising of external funding
  Targeted approach to available, IFI lending mechanisms in EE and urban sector
  Application of external financing with dedicated loan applications based on pre-feasibility studies

## Slide 6: The Multiple Benefits of Energy Efficiency
Sector | Example of energy efficiency measures | Multiple benefits
Municipal public buildings | Retrofit of public buildings such as schools, kindergartens and administrative buildings Improved building energy management | Increased room comfort and health Improved learning environment Increased lifetime and attractiveness of historic buildings
Street lighting | Upgrade of street lighting to LEDs Extension of street lighting including illumination of sidewalks, promenades, parks, etc. | Increased traffic safety Increased safety for predestines Improved attractiveness of sites for tourists and residents
Water supply and sanitation | Retrofit of potable water supply network Introduction of water metering for all consumers Rehabilitation of water pumping stations Introduction of active leak detection and pressure management to reduce water losses | Increased sanitary comfort More continuous water supply at adequate pressure Higher water availability to connect new customers
Solid waste | Optimization of waste collection routes and upgrade of collection vehicles Construction of waste transfer sorting, recycling and composting stations | Reduction of local air pollution Additional revenues from sale of recycled products Compliance with EU norms
Transport | Up-grade of public busses to low emission vehicles Promotion of cycling paths and establishment of bike renting system Historic site shuttle-bus service, mobility stations or a bus terminal with central parking | Reduced local air pollution Improvement of passenger comfort Reduced individual motorized transport in the city center Better access to historic sites for tourists and citizens

## Slide 7: Findings from Municipal Energy Diagnostics
Key Performance Indicators (TRACE) |  | 
Primary energy consumption per capita | 2,690 | kWh/capita/year
Electricity consumption per capita | 1,090 | kWhe/capita/year
Thermal energy consumption per capita | 1,200 | kWhT/capita/year
Primary energy consumption per GDP | 0.53 | kWh/USD of GDP, year
Electricity consumption per GDP | 0.21 | kWhe /USD of GDP, year
Specific energy consumption is comparatively at medium level and persuade in a direct benchmark with other municipalities a medium to good performance,
BUT
  It is because of a relatively low intensity of services (e.g. in schools and residential buildings) and low level of GDP per capita
  Not because of application of high efficient energy technologies at high energy service level.
 The picture turns to medium to low level of energy performance with high potentials for energy loss reduction and energy saving.

## Slide 8: Distribution of Final Energy Consumption
Total energy consumption amounted to 150 GWh in 2015 with 40% of the consumption being attributed to electricity.
Energy consumption of the residential sector constitutes approximately 73%.
Chart: GWh/yr
| Municipal buildings | Street lighting | Water/ Waste water | Waste | Public transport | Private transport | Other pubic buildings | Commercial | Residential sector
Power | 2.2835 | 0.48 | 1.2759 | 0 | 0 | 0 | 0.387 | 10.25 | 45.6765
Wood | 0.62535 | 0.0195 | 0.96875 | 43.1235
Diesel Gasoline | 0.5701 | 0.30346 | 21.6755 | 0 | 0 | 0
Fuel (Oil/gas/LPG) | 0.14213 | 0.0195 | 0.96875 | 20.535
Chart: 
| Power | Wood | Diesel Gasoline | Fuel (Oil/gas/LPG)
 | 60.3529 | 44.7371 | 22.5491 | 21.6654

## Slide 9
Relative
Energy
Intensity
Energy Spending
City Authority Control
X
X
Sector Prioritization

## Slide 10: Identification, Assessment and Selection of EE Measures
10
> 80
Options
Data Collection &
Preliminary Analysis
Beginning of
TRACE Assessment
Synthesizing Potential Programs
Pre-Feasibility Studies
Pilots, Fundraising, Feasibility
Implementing & Analyzing TRACE Tool
Technical Assistance & Investments
Implementation of Selected Interventions

## Slide 11: Relative Energy Intensity
Sector | Selected KPI |  | Performance | EE potential
Water supply & waste water | Energy density of water production Including individual power for pumping | 0.26 kWhe/m3 ~ 2.3 kWh/m³ | High Very low | 20-40% 60-80%
 | Percentage of non-revenue water | 71% | Very low | 60-80%
Street lighting | Annual electricity consumed per lit road | 18 kWhe/m | Medium | 50-60%
Public buildings | Annual energy consumption | 150 kWhth/m2 11 kWhel/m2 | Low, not meet demand | 30-50%
Transport | Public transport energy consumption | 0.2 MJ/pass km | Medium – to high | 10%
Public sector energy consumption in the 5 sectors amounts to 5.7 GWh/year, 4% of city wide energy
Chart: 
| Municipal buildings | Street lighting | Water/ Waste water | Waste | Public transport
 | 3.051 | 0.48 | 1.2759 | 0.5701 | 0.30346

## Slide 12: Energy Spending
Energy spending for municipal sector facilities (public buildings, street lighting, waste, water and transport ) amounts to 0.73 million USD
of which half is spent on energy supply for municipal buildings
representing 4 % of the annual municipal budget
Share of spending for energy, 2015, total 16.2 Million USD/year
Share of municipal spending for energy, 2015, total 0.73 Million USD/year
Chart: 
| Public Transport | Private Vehicles | Municipal Buildings | Street Lighting | Potable Water | Solid Waste | Residential sector | Commercial sector
 | 45623.413 | 3258815.2174 | 349512.6621 | 70121.7391 | 186397.4609 | 74563.0435 | 10452868.5706 | 1817593.5978
Chart: 
| Public Transport | Municipal Buildings | Street Lighting | Potable Water | Solid Waste
 | 45623.413 | 349512.6621 | 70121.7391 | 186397.4609 | 74563.0435

## Slide 13: Sector Prioritization
1. Municipal buildings
2. Potable water
3. Street lighting
4. Solid waste
5. Public transportation
Sector | Energy spending (in million USD including VAT) in 2015 | Energy Savings Potential = Relative Energy Intensity | Municipal level of control
Public Transportation | 45,623 | 10% | MEDIUM
Private Vehicles | 3,258,815 | 20% | LOW
Municipal public buildings | 349,513 | 30-50% | HIGH
Street Lighting | 70,122 | 60% | HIGH
Potable Water | 186,397 | 40-50% | HIGH
Waste Water |  | 0% | HIGH
Solid Waste | 74,563 | 30-40% | HIGH
Electricity sector |  | 5-10% | LOW
Residential sector | 10,452,869 | 40-50% | LOW
Commercial sector | 1,817,594 | 30% | LOW

## Slide 14
Sectoral energy use challenges and energy efficiency opportunities

## Slide 15: Municipal Buildings
Municipal Buildings Area, approximately | 19,000 | m2
Municipal Buildings Electricity Consumption | 11 | kWhe/m2,year
Municipal Buildings Heat Consumption | 150 | kWh/m2,year
Municipal Buildings Energy Spend as a % of Budget | 4% | %
Specific Challenges | Technical EE solutions
Building envelops need repair, roofs uninsulated; windows single glazed and partly damaged Insufficient heating during winter, partly due to fuel limits; heating in all kindergartens insufficient Different heating technologies such as electricity, wood and diesel; Insufficient lighting levels; Little or no hot water supply No building inventory Low maintenance capacities | (A) Building envelope measures: Insulation and repair of roof, replacement of windows and doors; on demand repairs on envelope, illumination of historic buildings (B) Inner-building EE measures: Lighting upgrades with LED (C) Heat generation facility (on demand after thermo-modernization): Installation of distributed ceramic heaters efficient wood ovens or where diesel boilers are installed fuel switch to pellet boiler, installation of solar hot water (kindergartens) ~ 80% of Facilities: 15 schools + 9 kindergartens

## Slide 16: Street Lighting
Light Points | 1,763 | 
Electricity Consumed per km of Lit Roads | 18,460 | kWhe/km,year
Electricity Consumed in Public Lighting | 480,000 | kWhe,year
Distance of Lit Roads | 26 | km
Specific Challenges | Technical EE solutions and project proposals
High diversity of lighting types and fixings (high maintenance) Partly old and outworn lamp covers Insufficient lighting levels, parts of cities without lighting Villages within municipal boundaries with poor or no lighting High awareness and priority of switching to efficient technologies To enhance the attractiveness of the museum zone, further historic building facades require an illumination | Standard EE measures: Replacement of current mercury and sodium luminaires with LED luminaries including dimming Projects of touristic relevance Replacement of high pressure mercury, sodium and CFL luminaires in the museum zone with LED luminaries (historic design) Replacement of CFL and sodium HP by LED at access road to castle Museum zone + Old Bazar, Gjirokastra Castle +Access road

## Slide 17: Water and Waste Water
Water Consumption Per Capita Per Day | 72 | L/capita/day
Energy Density of Water Production - Utility | 0.26 | kWhe/m3
Energy Density of Water supply- including end user | 2.3 | kWhe/m3
Percentage of Non Revenue Water | 71 | %
Share of costs for energy out of total costs | Up to 30 | %
Specific Challenges | Technical EE solutions
High water losses in distribution systems across cities > 70% Limited water supply due to losses (from 1-4 hours per day) High energy consumption at end- consumer to ensure uninterrupted individual water supply with individual storage tank and pump. Old and inefficient pumping equipment at pumping stations Leakages in water reservoirs Insufficient maintenance Villages without sewerage systems High impact for tourism sector, high investment implications | Water supply Rehabilitation of water supply network 75-80% of system covered under two stages of KfW loan. Water metering program (KfW) Prioritizing energy efficient water resources , 2 reservoirs (KfW) Upgrading of pumping stations Active leak detection and pressure management program Waste water (no EE effects, not in investment program) Retrofit and extension of waste water collector and sewer system (KfW phase II) Construction of waste water treatment plant

## Slide 18: Waste Collection and Disposal
Total Waste | 9,300 | tonnes/yr
Waste per Capita | 167 | kg/capita
Percentage of Solid Waste Recycled | 0 | %
Fuel consumption for waste collection | 50.000 570 | Liters MWh
Specific Challenges | Technical EE solutions
Existence of informal waste sites prevents interventions in waste collection (safeguards) Demand for regional landfills according to environmental standards Low per capita waste generation No sorting and recycling Distance between collection points and disposal sites contributes to high fuel costs No transfer stations Recyclable fragments of the official collected waste volume amount to 40-60%, | There is a need for reduction of waste volumes to be transported to landfill Waste vehicle fleet (3+3) retrofit or replacement program Construction of a waste transfer station Waste collection route optimization, including waste infrastructure planning, containers, collection routes, schedule and timing optimization, vehicles, control unit and preparation of separation Construction of modern landfill site + gas capture Extension of waste collection bins (underground in G. city center) with separation

## Slide 19: Motorized and Public Transportation
Public Transportation Mode Split | < 10 % | 
Public Transport Energy Consumption | 0.2 | MJ/passenger km
Public Transport Energy consumption | 1,100 | GJ
Passenger Kilometers | ~ 6 | million km
Specific Challenges | Technical EE solutions
Very low non-motorized transport High dependence on private vehicles Public transportation particularly relevant for tourism in heritage cities Car usage in historic centres discourages higher tourism activities: e.g. public parking spaces could be reused to support tourism development Low energy performing vehicles, (busses) age > 10 years Opportunity for development of measures to discourage car usage in historic parts and development of heritage trail shuttle | Shuttle-busses with clean traction system (e.g. electric) “Heritage trail” Route: castle-center/bazar-terminal, total 10 km round course, bus stations, points of interest, transport hubs and hotels 2 shuttle busses substitute taxi and individual car traffic Park + Ride terminal at central bus station, waiting area with information panel Establishment of bicycle renting system

## Slide 20: Municipal Energy Efficiency Plan 2030
14 EE investment measures in 5 municipal sectors, resulting in annual energy savings of 7.6 GWh, or 42 % compared to 2015 consumption (of which 60% result form the committed water sector measures)
Investment demand of 19.5 million USD (of which in the water sector up to 13 million USD can be covered by a KfW loan)
Overall payback time of the entire EE investment package is 11-12 years
Cumulative energy cost savings for the period 2017 to 2030 of approximately 40 million USD
Emissions reduction of 2,100 tones CO2 equivalent per year in 2030

## Slide 21: Matrix of Energy Efficiency Measures
Investment costs | Payback time < 5 years | 5-15 years | 15-25 years
0-200,000 USD | SL-01: Replacement of HP mercury, sodium and CFL in the museum zone with LED (historic design) PW-03: Upgrading of pumping stations PW-04: Active Leak Detection and Pressure Management Program | PB-03: Replacement of indoor lighting for all municipal public buildings SL-03: Replacement of CFL and sodium HP by LED at access road to castle | 
200,000 – 1 Million USD |  | SL-02: Replacement of HP mercury, sodium and CFL luminaires outside the museum zone with LED PW-05: Prioritizing of EE Water Resources (2 water reservoirs) MW-01: Waste vehicle fleet replacement program MW-02: Construction of waste transfer station and underground containers | PW-02: Water meter program PT- 02: No-emission shuttle-busses “Heritage trail”
Above 1 Million USD |  | PW-01: Retrofit of water supply network | PB-01: Complex retrofit of 80% of schools & kindergartens PB-02: Complex retrofit of historic public buildings incl. facade illumination

## Slide 22: Sectoral Savings Targets and Benefits until 2030
Municipal public buildings
At least 30% energy saving of heat energy for all facilities (schools, kindergartens) by retrofit 50% energy saving for domestic lighting by retrofit to LED Use of renewable energy to cover 50% of hot water demand
Street lighting
At least 60% energy savings for the complete public lighting system
Water supply & Waste water
At least 60% reduction of water losses 30 % electricity savings at pumping stations for water supply At least 80% of waste water is collected and those volumes are cleaned and treated
Public transportation
Increase of urban mobility by improvement of service and attractiveness of public transport Up to 50% reduction of individual motorized transport by in the historic city center by increasing the attractiveness of public transport as alternative to individual cars
Waste management
100% reduction of illegal dumped waste volume by increase of the waste collection rate Minimum of 50% of the waste volume is sorted and prepared for recycling or composting Reduction of 25% the fuel consumption for waste collection vehicles

## Slide 23: Ongoing Local Investment Programs
Sector | Project | Donor/ Financier | Current stage
Water supply | Prioritizing efficient water resources, 2 reservoirs | KfW | Phase I:completion in 12/2016
 | Retrofit of water supply network (75-100%) | KfW | Phase I: completion in I/2017 Phase II: 2017 / 2018
 | Water metering | KfW | Phase II: currently under design
Waste water | WW collectors and sever network | KfW | Phase II: currently under design
Waste | Landfill site | Min. Urban Dev | Feasibility study, tendering in 2017
Buildings | Retrofit of historic building facades in bazar street | AADF | Design stage
 | Retrofit of City hall building | EU IPA | Under implementation
Street lighting | Illumination of historic bazar area by LED | AADF | Feasibility study , 2016 Currently preparation for tendering
 | Illumination of historic bazar area by LED | GiZ | Feasibility study , 2015
Traffic | Parking and city road reconstruction - bazar street | AADF | Concept stage

## Slide 24: Financial Analysis
Investment costs (orange) compared to 25 years cost savings (yellow)
Chart: 
| Municipal buildings | Street lighting | Potable water | Municipal waste | Public transport
Investment costs (M USD) | 3.0829 | 0.9398 | 13.8304 | 0.6125 | 1
25 yrs Energy Cost savings (M USD) | 3.4438 | 3.0599 | 31.0953 | 2.4739 | 1.1657
Chart: Specific energy savings in kWh per USD investment
| Municipal buildings | Street lighting | Potable water | Municipal waste | Public transport
Specific EE kWh/USD | 0.35677 | 0.33505 | 0.4173 | 0.32577 | 0.24177

## Slide 25: Annual Financing Demand and Energy Savings
Annual energy saving achievements in GWh/yr
Chart: Million USD
| 2017 | 2018 | 2019 | 2020 | 2021 | 2022 | 2023 | 2024 | 2025
Municipal buildings | 0.15415 | 0.61658 | 0.61658 | 0.46243 | 0.46243 | 0.46243 | 0.30829 | 0 | 0
Street lighting | 0.14097 | 0.04699 | 0.04699 | 0.04699 | 0.04699 | 0.04699 | 0.04699 | 0.04699 | 0.4699
Potable water | 4.8406 | 3.4576 | 3.4576 | 2.0746 | 0 | 0 | 0 | 0 | 0
Municipal waste | 0.06125 | 0.06125 | 0.06125 | 0.1225 | 0.1225 | 0.06125 | 0.06125 | 0
Public transport | 0 | 0 | 0.5 | 0.5 | 0 | 0 | 0 | 0 | 0
Financing demand for implementation of the energy efficiency plan
Chart: 
| 2017 | 2018 | 2019 | 2020 | 2021 | 2022 | 2023 | 2024 | 2025
Municipal buildings | 0 | 0.054994 | 0.27497 | 0.49494 | 0.65992 | 0.82491 | 0.98989 | 1.0999 | 1.0999
Street lighting | 0 | 0.047232 | 0.062975 | 0.078719 | 0.094463 | 0.11021 | 0.12595 | 0.14169 | 0.15744
Potable water | 0 | 2.02 | 3.4629 | 4.9057 | 5.7714 | 5.7714 | 5.7714 | 5.7714 | 5.7714
Municipal waste | 0 | 0.019954 | 0.039907 | 0.059861 | 0.099768 | 0.13968 | 0.15963 | 0.17958 | 0.17958
Public transport | 0 | 0 | 0 | 0.12088 | 0.24177 | 0.24177 | 0.24177 | 0.24177 | 0.24177

## Slide 26: Investment Costs and Savings by Sector
Contribution to annual energy savings
Chart: 
| Municipal buildings | Street lighting | Potable water | Municipal waste | Public transport
Energy Saving in (GWh/year) | 1.0999 | 0.31488 | 5.7714 | 0.19954 | 0.24177
Chart: Investment costs (M 19.5 USD)
| Municipal buildings | Street lighting | Potable water | Municipal waste | Public transport
Investment costs (M USD) | 3.0829 | 0.9398 | 13.8304 | 0.6125 | 1

## Slide 27: Energy Consumption 2015 vs. 2030
Energy savings of 7.6 GWh in 2030 represent 5 % of the overall energy consumption in the Municipality of Gjirokastra for 2015 (150 GWh).
Chart: 
| Municipal buildings | Street lighting | Potable water | Municipal waste | Public transport
Energy consumption in 2015 (GWh/yr) | 3.051 | 0.48 | 13.8594 | 0.5701 | 0.30346
Energy consumption after EE program (GWh/yr) | 1.9511 | 0.16512 | 8.088 | 0.37057 | 0.061689

## Slide 28: Implementation strategy
Strengthening energy efficiency delivery capacity
Promoting sustainable energy efficiency financing
Scaling up municipal energy efficiency investments
A critical requirement for the successful implementation of a municipal energy efficiency plan is the ownership and commitment of the municipal stakeholders.

## Slide 29: Strengthening EE Delivery Capacity
A critical requirement for successful energy efficiency program implementation plan is to build up institutional capacities and to create a focal point for energy efficiency in the municipality.
It is recommended to establish a dedicated municipal department for energy efficiency within the municipality.
SET-UP Mandate & Statute Stakeholder commitment & collaboration agreements Access to data Rights and legitimacy
REQUIREMENTS
CAPACITIES
Coordination & Facilitation project preparation Information & Promotion Monitoring & Evaluation Program implementation support
Business plan Organization chart Funding Technical Assistance
Qualified staff Instruments & tools Local network Twinning arrangements
TASKS

## Slide 30: Sustainable Energy Efficiency Financing
Financing solutions can be divided into the following basic categories:
budget appropriations, or financing through internal capital budgets,
grant financing received by public agencies,
debt financing to public agencies,
Private sector or third party (debt or equity) financing including energy performance contracting.
Steps to develop projects for dedicated financing
Identify EE opportunities
Identify available energy efficiency financing options
Analyze the specific requirements of possible financiers
Assess the ability of potential projects to meet these requirements
Design the project and financing application to meet the above requirements
Apply for financing

## Slide 31: Timeline for Implementation
Scaling up municipal energy efficiency investment |  |  | Promoting sustainable energy efficiency financing |  | Strengthening energy efficiency delivery capacity
Tasks within next 12 months |  |  |  |  | 
Adoption of the energy efficiency program by municipal council Preparation of a targeted EE investment program Implementation supervision, completion and commissioning of pilot projects Awareness raising and EE promotion programs |  | Life-cycle cost assessment and procurement guidelines |  | Designation of responsible staff for implementation of energy efficiency program Establishment of Municipal energy efficiency service department or energy office Designation of an energy efficiency task force and facility energy managers Development of a municipal building inventory | 
Tasks within year 2-3 |  |  |  |  | 
Implementation investment programs Elaboration of feasibility studies for investment projects which have a realistic chance for financing | Apply for funds (grants and loans) from national and international sources very targeted, prepared and justified |  |  | capacities for the implementation and monitoring and verification of the program; Setting and monitoring of EE targets in public facilities, with mandatory submission of annual plans | 
Tasks within years 4-10 |  |  |  |  | 
Periodic energy audits to identify cost-effective energy efficiency measures Extension of the pipeline for energy efficiency investment projects |  |  |  |  | Cross sector information and awareness raising on energy efficiency.

## Slide 32: Questions and next steps
  DECISIONS
    Sector priorities
    Preliminary list of EE measure
    EE targets
    Set-up of municipal energy management
NEXT STEPS
  WBG team:
  Review of the catalogue of EE measures (according to todays decisions)
  Completion of EE plan
  Pre-feasibility analysis of selected EE measures (street lighting)
  Municipality of Gjirokastra:
  Confirmation of ownership of the municipal EE plan, preparation for adoption by Municipal Council
  Institutional set-up of EE department
  OPEN QUESTIONS

## Slide 33
Thanks to all members of the municipal administration and service utility team who contributed to the successful completion

## Slide 34
ADDITIONAL SLIDES

## Slide 35: Municipal Energy Efficiency Plan
Following assumptions have been taken for the preliminary assessment of EE measures
Investment costs at the level of 2016 prices, including import duties (on demand), installation, using the currency exchange rate of December 31, 2015 (1 USD = 115 ALL)
Emission factors for primary energy carriers
Payback is preliminarily calculated on the basis of annually saved energy costs. For this purpose the 15-year average tariff of the respective final energy carrier is used for the period 2015 to 2020 (annual escalation rates of 3 % in average)
The implementation period of the EE measure starts in 2017, with delivery of EE benefits in the year 2018 the earliest. Each EE measure is completed in 2025 (depending on the complexity of each measure) EE benefits become valid in the energy balance of 2025.
Key assumptions and Projection of energy tariffs/costs
Chart: Energy costs for public entities (USD per kWh) 20 yrs average 2017-2032
| Power-peak | Power-off-peak | Diesel | Wood | Mazut | LPG
 | 0.23946 | 0.20822 | 0.21429 | 0.014851 | 0.09438 | 0.19519
Chart: Energy cost development forcast
| 2016 | 2017 | 2018 | 2019 | 2020 | 2021 | 2022 | 2023 | 2024 | 2025 | 2026 | 2027 | 2028 | 2029 | 2030 | 2031 | 2032 | 2033 | 2034 | 2035 | 2036 | 2037 | 2038 | 2039 | 2040 | 2041 | 2042 | 2043 | 2044 | 2045
Electricity peak | 0.17304 | 0.17823 | 0.18358 | 0.18909 | 0.19476 | 0.2006 | 0.20662 | 0.21282 | 0.2192 | 0.22578 | 0.23255 | 0.23953 | 0.24671 | 0.25412 | 0.26174 | 0.26959 | 0.27768 | 0.28601 | 0.29459 | 0.30343 | 0.31253 | 0.32191 | 0.33156 | 0.34151 | 0.35175 | 0.36231 | 0.37318 | 0.38437 | 0.3959 | 0.40778
Electricity off-peak | 0.15047 | 0.15498 | 0.15963 | 0.16442 | 0.16935 | 0.17444 | 0.17967 | 0.18506 | 0.19061 | 0.19633 | 0.20222 | 0.20829 | 0.21453 | 0.22097 | 0.2276 | 0.23443 | 0.24146 | 0.2487 | 0.25616 | 0.26385 | 0.27176 | 0.27992 | 0.28832 | 0.29696 | 0.30587 | 0.31505 | 0.3245 | 0.33424 | 0.34426 | 0.35459
Diesel | 0.15486 | 0.1595 | 0.16429 | 0.16922 | 0.17429 | 0.17952 | 0.18491 | 0.19045 | 0.19617 | 0.20205 | 0.20811 | 0.21436 | 0.22079 | 0.22741 | 0.23423 | 0.24126 | 0.2485 | 0.25595 | 0.26363 | 0.27154 | 0.27969 | 0.28808 | 0.29672 | 0.30562 | 0.31479 | 0.32423 | 0.33396 | 0.34398 | 0.3543 | 0.36493
LPG | 0.14105 | 0.14528 | 0.14964 | 0.15413 | 0.15875 | 0.16351 | 0.16842 | 0.17347 | 0.17867 | 0.18404 | 0.18956 | 0.19524 | 0.2011 | 0.20713 | 0.21335 | 0.21975 | 0.22634 | 0.23313 | 0.24012 | 0.24733 | 0.25475 | 0.26239 | 0.27026 | 0.27837 | 0.28672 | 0.29532 | 0.30418 | 0.31331 | 0.32271 | 0.33239
Heavy fuel oil | 0.068202 | 0.070249 | 0.072356 | 0.074527 | 0.076762 | 0.079065 | 0.081437 | 0.08388 | 0.086397 | 0.088989 | 0.091658 | 0.094408 | 0.09724 | 0.10016 | 0.10316 | 0.10626 | 0.10944 | 0.11273 | 0.11611 | 0.11959 | 0.12318 | 0.12688 | 0.13068 | 0.1346 | 0.13864 | 0.1428 | 0.14708 | 0.1515 | 0.15604 | 0.16072
Wood | 0.010732 | 0.011054 | 0.011386 | 0.011727 | 0.012079 | 0.012441 | 0.012815 | 0.013199 | 0.013595 | 0.014003 | 0.014423 | 0.014856 | 0.015301 | 0.01576 | 0.016233 | 0.01672 | 0.017222 | 0.017738 | 0.018271 | 0.018819 | 0.019383 | 0.019965 | 0.020564 | 0.021181 | 0.021816 | 0.02247 | 0.023145 | 0.023839 | 0.024554 | 0.025291

## Slide 36: Municipal energy diagnostic
The initial phase of the program is guided by and feedback from the municipality enabled the team to draft an energy efficiency (EE) program
TRACE - Tool for Rapid Assessment of City Energy
Sector
Assessment
Energy Efficiency Recommendations
Intervention
Models
Done
Done
Level of Activity
Progress
Done

## Slide 37: City Authority Control
Sector | Municipality authority level of power |  | 
 | Regulatory | Budget control | Influence & enforcement
Public transport | MEDIUM | LOW | MEDIUM
Private transport | LOW | LOW | LOW
Public, municipal buildings | HIGH | HIGH | HIGH
Street lighting | HIGH | HIGH | HIGH
Potable water / waste water | HIGH | HIGH | HIGH
Solid waste | HIGH | HIGH | HIGH
Power supply | LOW | LOW | LOW
Residential sector | LOW | LOW | MEDIUM
Commercial sector | LOW | LOW | LOW