## Slide 1: Findings from technical visits to Saranda, Gjirokastra, Permet and Berat
ALBANIA
Project for Integrated Urban and Tourism Development (PIUTD)

## Slide 2: Agenda
Overview of visits
Identified priority sectors
Identified EE challenges and opportunities by sector
Preliminary recommendations for investment projects
Next steps

## Slide 3: Summary of visits to cities, Sept. 13-23
Cities show high commitment and ownership in tackling energy efficiency opportunities. Collaboration was fruitful and most of the data could be collected.
Meetings with mayors, municipal services, budget, tourism and technical departments and municipal utilities helped to clarify sectoral energy use challenges and data gaps and develop a sense of local priorities
Technical visits at public buildings, water infrastructure and street lighting contributed to a better understanding of technical performance and investment demands
The kick-off workshop was used to explain approach, targets and data requirements for a successful planning of potential measures
It contributed to establishing a cross-sectoral working group and common ownership for a municipal energy savings plan among participating staff

## Slide 4: Sector priorities at a glance
 | Saranda | Gjirokastra | Permet | Berat
Municipal buildings | High | High | High | Moderate
Street lighting | High | High | High | High
Water supply | Low (KfW) | Low (KfW) | High | Low (KfW)
Waste water | High (KfW) | High | High | Low (KfW)
Solid waste | High (C), regional landfill | High, informal landfill | High, informal landfill | Moderate (SECO)
Public transport | Moderate | High | Low | High

## Slide 5: EE challenges and opportunities
Municipal Buildings
  Insufficient heating during winter, partly due to consumption limits and poor insulation; heating in all kindergartens insufficient
  Different heating technologies such as electricity, wood and diesel;
  Insufficient lighting, little or no hot water supply, poor kitchen equipment, dangerous installations
  Building envelops need repair, roofs uninsulated; windows outworn and partly damaged
  Average low maintenance capacities, meanwhile in Berat very good service capacity
Saranda | Gjirokastra | Permet | Berat
Public buildings require indoor lighting upgrades, schools without heating | Many buildings in need for capital repair, opportunity to contribute to touristic attraction | Kindergartens need energy efficiency upgrades, all other public buildings in good condition, local capacity available | Replacement of inefficient wood stoves and installation of solar hot water, lighting upgrades. High maintenance capacity.

## Slide 6: EE challenges and opportunities
Street Lighting
Depending on city only partly operational
Partly old and outworn lamp covers
Majority of cities with insufficient lighting levels, parts of cities without lighting
High diversity of lighting types and fixings (high maintenance)
Villages within municipal boundaries with poor or no lighting
High awareness and priority of switching to efficient technologies
Ease and speed of implementation (fast-track)
Saranda | Gjirokastra | Permet | Berat
Tourist village of Ksamil has high demand for public lighting upgrade; castle illumination could be considered | Uncertainty because of AADF interventions in historic center but remaining parts of historic center could be addressed; partly EE modernization of street lighting | EE modernization of street lighting | Lighting of two access roads to castle as well as improvement of lighting and illumination in historic center, EE modernization of main street lighting

## Slide 7: EE challenges and opportunities
Water supply
High water losses in distribution systems across cities >60%
Limited water supply due to losses (from 1-12 hours per day)
Need to operate water pumps and tanks on buildings to ensure water supply at dwellings
High electricity consumption and hence high potential electricity savings
Old and inefficient pumping equipment at pumping stations
Leakages in water reservoirs
Insufficient maintenance
KfW operations in Saranda, Gjirokastra and Berat
Saranda | Gjirokastra | Permet | Berat
First stage (45%) covered under KfW loan, 2nd stage not covered. | 100% of system covered under two stages of KfW loan. | No donor engagement but high demand for system upgrade. | 100% of system covered under two stages of KfW loan.

## Slide 8: EE challenges and opportunities
Wastewater
Coverage of sewerage systems across all cities >50%
In Berat, Gjirokastra and Permet wastewater is currently discharged into local rivers
Majority of villages without sewerage systems in all municipalities
Water treatment systems exist only in Saranda but equipment partly not operational while Ksamil connection to WWTP expected in December
High impact for tourism sector, high investment implications
Lack of capacity for operation of WWTP at municipal level
KfW commitment in three cities
Saranda | Gjirokastra | Permet | Berat
Missing waste water pumps from prior World Bank program, Ksamil connection to WWTP upcoming. | Use of septic tanks in old part of the city, no WWTP, sewerage currently discharged into the river. | No WWTP, sewerage currently discharged into the river. | No WWTP, sewerage currently discharged into the river.

## Slide 9: EE challenges and opportunities
Public Transportation
Public transportation crucial in all cities but particularly relevant for tourism in heritage cities
Car usage in historic centres discourages higher tourism activities in areas: public parking spaces could be reused to support tourism development
Citizens living in historic centres rely on cars but could be encouraged to switch to less invasive transportation
Opportunity for shuttle buses (e.g. electric buses) to connect points of interest
Saranda | Gjirokastra | Permet | Berat
Outworn and unsafe intercity buses with connection to Butrint and Ksamil with high relevance for tourism sector. | Opportunity for development of a Park and Ride system next to national road and development of heritage trail shuttle. | n.a. | Opportunity for development of measures to discourage car usage in historic parts and development of heritage trail shuttle.

## Slide 10: EE challenges and opportunities
Municipal Solid Waste Management
Existence of informal waste sites in majority of cities prevents interventions in waste collection (safeguards)
Demand for regional landfills according to environmental standards
Low per capita waste generation
No sorting and recycling takes place in any of the cities
Distance between collection points and disposal sites contributes to high fuel costs in Saranda
No transfer stations
Opportunity to optimize waste collection routes
Saranda | Gjirokastra | Permet | Berat
Access to regional landfill (Vlora), professional contractor operates in the city but duration of contract limited to 1 year. | Informal landfill and illegal dumping, old hauling equipment. | Informal landfill and illegal dumping, old hauling equipment. | Plans to develop a landfill at the regional level. Currently, informal dumping sites.

## Slide 11: Suggested key criteria for project selection
Identification & Selection
Priority by city and contribution to tourism development |  | Payback time < life time | 
Energy savings > 30% (depending on sector) |  | Savings to municipal budget (surplus vs. receiving city) | 
WB safeguards eligibility (e.g. resettlements, informal landfill) |  | Local availability and appropriateness of materials and technologies (e.g. insulation, boiler) | 
High co-benefits (e.g. health, safety, emissions) |  | Ease of implementation | 

## Slide 12: Catalogue of potential measures
Schools and Kindergartens Saranda, Gjirokastra, Permet and Berat
Technical solutions
(A) Building envelope measures:
Insulation and repair of roof, replacement of windows and doors; on demand repairs on envelope, illumination of historic buildings
(B) Inner-building EE measures:
Lighting upgrades and replacement of wiring
(C) Heat generation facility (on demand after thermo-modernization):
Installation of distributed ceramic heaters, efficient wood ovens or where diesel boilers are installed fuel switch to pellet boiler, installation of solar hot water systems (kindergartens only)
Specific Investment costs: up to 100 EUR/m²

## Slide 13: Profile of potential lighting projects
Ksamil, Municipality of Saranda
Technical solution
Replacement of current poles and luminaires along the 1,5 km promenade with high performing LED luminaries. Majority of current poles and luminaires is damaged. This measure should be accompanied by refurbishment of promenade, installation of new wiring and proper drainage for promenade.
Specific investment costs:
800 EUR per light point incl. pole for a total of 75, approx. 60,000 EUR
60-70 EUR per meter, approx. 100,000 EUR for rehabilitation of promenade

## Slide 14: Catalogue of potential lighting projects
Saranda, Gjirokastra, Permet and Berat
Technical solutions
Lighting of access road to historic monuments (Castle Berat)
Improvement of lighting in the historic centers or pedestrian zones (Gjirokastra and Berat)
Energy efficient lighting in main streets (partly but all cities)
Decorative illumination of historic monuments/buildings (Berat, Gjirokastra, Saranda)
Specific Investment costs:
- 800 - 1,200 EUR per lighting point (excluding/ including new pole) plus refurbishment works
- For decorative illumination approx. 2,000 EUR per object (average 50 objects per city district)

## Slide 15: Profile of potential tourism transportation projects
Berat and Gjirokastra
Technical solution
Development of a park and ride system that combines inner city public transportation with tourism activities. Waiting areas and bus stations at points of interest and economic hotspots along with establishment of an information system.
Specific Investment costs:
0.5 M EUR for a package of 1 electric shuttle bus including infrastructure, such as charging station, waiting areas, stations, information system.

## Slide 16: Catalogue of potential water and wastewater projects
Technical solution water supply
Replacement of water supply pumping stations (all cities)
Rehabilitation of main water storages (all cities)
Water distribution system rehabilitation and extension of water metering (Permet only)
Technical solution waste water
Full rehabilitation of collecting and sewerage
system (Permet and Gjirokastra)
New waste water treatment plants
(Gjirokastra and Permet)
Pump and motor replacement in WB WWTP (Saranda only)
Specific Investment costs:
Water pumping station approx. 30,000 - 50,000 EUR
Water distribution system, approx. 0.5 M EUR per km
200 EUR per water meter

## Slide 17: Potential investment projects finance demand
 | Saranda | Gjirokastra | Permet | Berat
Water supply | Connection between reservoir and storage for one district Vrion pumping station retrofit |  | Distribution network and storage rehabilitation | Replacement of old equipment in 15 pumping stations
Wastewater | Wastewater pumps and ventilation motors at WWTP | Sewerage system and WWTP (?) | Sewerage system and WWTP | 
Municipal buildings | EE rehabilitation and lighting upgrades in buildings | EE rehabilitation of heritage buildings incl. illumination | EE rehabilitation of four kindergartens | Replacement of wood stoves, solar water heating, lighting upgrades
Street lighting | Promenade and lighting upgrade in Ksamil | Luminaire replacement and extension with LED in historic district (AADF) | Luminaire replacement and extension with LED | Luminaire replacement on two roads and SL and illumination of two historic districts
Urban public transportation | Extension of pedestrian zone in Saranda and cycling infrastructure, replacement of two shuttle buses (Butrint) | Development of park and ride system and heritage trail incl. shuttle bus |  | Development of park and ride system and heritage trail, cycling infrastructure

## Slide 18: Preliminary investment demand by city, EUR
Chart: 
| Saranda | Gjirokastra | Permet | Berat
Water supply | 400000 | 3000000 | 450000
Wastewater | 100000 | 5000000 | 3500000
Municipal buildings | 3200000 | 3000000 | 2200000 | 200000
Street lighting | 400000 | 500000 | 400000 | 700000
Urban public transportation | 1600000 | 1000000 | 1000000

## Slide 19: Preliminary investment demand by sector, EUR
Chart: 
| Water supply | Wastewater | Municipal buildings | Street lighting | Urban public transportation
Saranda | 400000 | 100000 | 3200000 | 400000 | 1600000
Gjirokastra | 5000000 | 3000000 | 500000 | 1000000
Permet | 3000000 | 3500000 | 2200000 | 400000
Berat | 450000 | 200000 | 700000 | 1000000

## Slide 20: Questions and next steps
  Open Questions
  Demand for coordination with other donor projects (sectors and cities covered) to avoid overlapping activities
  Technical assistance for local capacity building (ADF & donors)
Next steps
  Analysis of pilot projects and discussion with PIUTD team
  Decision workshop (November) to prioritize sectors and specific EE measures
  City background and EE assessment report (January)
  Pre-feasibility studies for fast-track lighting investments in Gjirokastra and Berat (February)